## Slide 1: Complex but Repeatable Growth Process
Many ways to grow graphene; Face to Face Growth
Produces SEG – semiconducting epigraphene which is well ordered buffer
Two silicon carbide chips sandwiched together; silicon face on top and carbon face on bottom
The sandwich is then baked in a leaky crucible at varying high temperatures in vacuum and in Argon
Silicon sublimates leaving behind carbon rich surface
Carbon rich surface crystalizes into graphene on the carbon face and into SEG on the silicon face
Temperature difference between the chips causes mass flow from bottom chip to top chip – facilitates growth
Can be patterned and gated to produce more complex electronics
Image from Zhao, J., Ji, P., Li, Y. et al.
AFM
Large flat surfaces
Leave this slide unchanged for reference
Put your names here

## Slide 2: Complex but Repeatable Growth Process
Many ways to grow graphene; Face to Face Growth
Produces SEG – semiconducting epigraphene which is well ordered buffer
Two silicon carbide chips sandwiched together; silicon face on top and carbon face on bottom
The sandwich is then baked in a leaky crucible at varying high temperatures in vacuum and in Argon
Silicon sublimates leaving behind carbon rich surface
Carbon rich surface crystalizes into graphene on the carbon face and into SEG on the silicon face
Temperature difference between the chips causes mass flow from bottom chip to top chip – facilitates growth
Can be patterned and gated to produce more complex electronics
Image from Zhao, J., Ji, P., Li, Y. et al.
AFM
Large flat surfaces
Change this slide